## Slide 1: Transition from RN to IRI Warranty Projects

## Slide 2: Data Source
Three year old PCS data collected from 2013 to 2017 (last five years of available data)
Data notes:
  Year of construction determined from acceptance
  Pavement age determined when PCS survey is conducted
  PCS data collected in lane with most distress; typically outermost lane

## Slide 3: RN Distribution after Three Years
Chart: Ride Number
 | 0 | 3
% Lane Miles with RN<3.5
All systems = 1.4%
Primary = 1.7%
Limited Access = 0.9%
RN=3.5

## Slide 4: IRI Distribution after Three Years
Chart: IRI (in/miles)
Statistic | All Systems | Primary | Limited Access
1st Quartile | 44 | 45 | 41
Median | 51 | 53 | 48
Weighted Mean* | 54 | 57 | 50
3r Quartile | 61 | 64 | 56
*weighted based on lane miles |  |  | 

## Slide 5: IRI(RN<3.5) Based on % Lane Miles
IRI (in/mi) | All Systems | Primary | Limited Access
>95 | 2.6 | 3.8 | 0.8
>100 | 2.0 | 2.9 | 0.6
>105 | 1.4 | 2.1 | 0.4
>110 | 1.0 | 1.5 | 0.3
IRI based on RN(<3.5) lane miles
  All systems, RN(<3.5)=1.4%: IRI>105 in/miles
  Primary, RN(<3.5)=1.7%: IRI>109 in/miles
  Limited Access, RN(<3.5)=0.9%: IRI>94 in/miles

## Slide 6: Average IRI over Three Year Period
Year | All Systems | Primary | Limited Access
0 | 49 | 49 | 48
1 | 51 | 52 | 48
2 | 53 | 55 | 50
3 | 54 | 56 | 50
Total Δ | 5 | 7 | 2
Δ + Acceptance R&R (95in/mile) | 100 | 102 | 97