## MAINTENANCE OF TRAFFIC.

(REV 10-28-14) (1-15)

SUBARTICLE 102-3.1 is deleted and the following substituted:

102-3.1 Beginning Date of Contractor’s Responsibility: Maintain traffic starting the day work begins on the project, on the first day Contract time is charged, or on the day work begins on the work order, whichever is earlier.

ARTICLE 102-11 is expanded by the following new Subarticles:

102-11.23 Necessary Maintenance Services (Straight Time): This item shall be used when using labor on Monday through Thursday. Time begins when the contractor’s personnel starts performing MOT duties. This pay item does not include traveling to and from work sites.  Time shall begin when the contractor or their personnel notifies the Engineer or their representative that set up is complete and they are ready to begin flagging operations and/or maintenance of devices. The contractor or their personnel will notify the Engineer or their representative when straight time ends and set-up or take-down begins. The contractor will be required and compensated for providing only one person to maintain the devices, unless otherwise directed by the Engineer.

102-11.24 Necessary Maintenance Services (Over Time): This item shall be used when using labor on Fridays through Sunday and holidays.  Time begins when the contractor personnel starts performing MOT duties. This pay item does not include traveling to and from work sites.  Time shall begin when the contractor or their personnel notifies the Engineer or their representative that set up is complete and they are ready to begin flagging operations and/or maintenance of devices. The contractor or their personnel will notify the Engineer or their representative when over time ends and set-up or take-down begins. The contractor will be required and compensated for providing only one person to maintain the devices, unless otherwise directed by the Engineer.

102-11.25 Emergency Maintenance of Traffic: The contractor will be compensated for setting up and taking down the devices. The contractor will be compensated for one Maintenance of Traffic pay item per work document. This pay item will only be used when a work order is issued with a start date of less than 72 hours.  Notification for work orders issued with notification of 72 hours or more before the start date will be considered incidental to the pay items on the work order, and no separate payment will be made therefore. Mobilization and all other cost incurred will be considered incidental to this pay item. No other pay items will be used.

102-11.26 Off Duty Law Enforcement Officer: The contractor will be compensated per hour the officer is at the work site in accordance with the work document and/or as requested by the Engineer or their representative.  Travel time is not included.

102-11.27 Truck Mounted Attenuator: Payment will be made per day as stated in the work document or as directed by the Engineer or their representative.  This pay item will be paid per day regardless of the number of locations work is performed at each site.

ARTICLE 102-12 is deleted.

ARTICLE 102-13 is deleted and the following substituted:

102-13 Basis of Payment.

102-13.1 Maintenance of Traffic (General Work): When an item of work is included in the proposal, price and payment will be full compensation for all work and costs specified under this Section except as may be specifically covered for payment under other items.

When the proposal includes a separate item of payment for this work, the work and incidental costs specified as being covered under this Section will be paid for at the contract unit price for the item of Mobilization.

When the proposal includes a separate pay item for Mobilization - Lump Sum, partial payment will be prorated based on the percentage of contract amount earned for work completed and accepted by the Department.

102-13.2 Traffic Control Officers: Price and payment will be full compensation for the services of the traffic control officers.

102-13.3 Special Detours: Price and payment will be full compensation for providing all detour facilities shown in the Plans and all costs incurred in carrying out all requirements of this Section for general MOT within the limits of the detour, as shown in the Plans.

102-13.4 Commercial Materials for Driveway Maintenance: Price and payment will be full compensation for all work and materials specified for this item, including specifically all required shaping and maintaining of driveways.

102-13.5 Work Zone Signs: Price and payment will be full compensation for all work and materials for furnishing signs, supports and necessary hardware, installation, relocating, maintaining and removing signs.

102-13.6. Business Signs: Price and payment will be full compensation for all materials and labor required for furnishing, installing, relocating, maintaining, and removing the signs as well as the cost of installing any logos provided by business owners.

102-13.7 High Intensity Warning Lights: Price and payment will be full compensation for furnishing, installing, operating, relocating, maintaining and removing high intensity flashing lights (Type B).

102-13.8 Channelizing Devices: Prices and payment will be full compensation for furnishing, installing, relocating, maintaining and removing the channelizing devices, including the costs associated with attached warning lights as required.

102-13.9 Barrier Wall (Temporary): Price and payment will be full compensation for furnishing, installing, maintaining, and removing the barrier. When called for, barrier wall (temporary) (relocate) will be full compensation for relocating the barrier.

102-13.10 Barrier Delineators: No separate payment will be made for barrier delineator installed on top of temporary barrier wall. The cost of furnishing, installing and maintaining the barrier delineators will be included in the cost of the temporary barrier wall.

102-13.11 Glare Screen (Temporary): Price and payment will be full compensation for furnishing, installing, maintaining, and removing the glare screen certified as installed/used on the project. When called for, glare screen (relocate) will be full compensation for relocating the glare screen.

102-13.12 Temporary Crash Cushion (Redirective/Gating): Price and payment will be full compensation for furnishing, installing, maintaining and subsequently removing such crash cushions. Payment for restoring damaged crash cushions will be the manufacturer’s/distributor’s invoice price for the new materials/parts plus 20% markup. The 20% markup is compensation for all necessary work including; but not limited to, labor, equipment, supplies and profit, as authorized by the Engineer. Additional MOT required for the repair of the crash cushion will be paid for under the appropriate MOT pay item.

102-13.13 Temporary Guardrail: Price and payment will be full compensation for furnishing all materials required for a complete installation, including end anchorage assemblies and any end connections to other structures and for installing, maintaining and removing guardrail.

102-13.14 Arrow Board: Price and payment will be full compensation for furnishing, installing, operating, relocating, maintaining and removing arrow boards.

102-13.15 Portable Changeable Message Sign: Price and payment will be full compensation for furnishing, installing, operating, relocating, maintaining and removing portable changeable message signs.

102-13.16 Portable Regulatory Signs: Price and payment will be full compensation for furnishing, installing, relocating, maintaining and removing a completely functioning system as described in these Specifications portable regulatory signs. Price and payment will be full compensation for furnishing, installing, operating, relocating, maintaining and removing portable regulatory signs.

Payment will include all labor, materials, incidentals, repairs and any actions necessary to operate and maintain the unit at all times that work is being performed or traffic is being affected by construction and/or MOT operations.

102-13.17 Radar Speed Display Unit: Price and payment will be made only for a completely functioning system as described in these specifications. Payment will include all labor, hardware, accessories, signs, and incidental items necessary for a complete system. Payment will include any measurements needed to insure that the unit conforms to all specification requirements.

Payment will include all labor, materials, incidentals, repairs and any actions necessary to operate and maintain the unit at all times that work is being performed or traffic is being affected by construction and/or MOT operations. Price and payment will be full compensation for furnishing, installing, operating, relocating, maintaining and removing radar speed display unit.

102-13.18 Temporary Signalization and Maintenance: Price and payment will constitute full compensation for furnishing, installing, operating, maintaining and removing temporary traffic control signals including all equipment and components necessary to provide an operable traffic signal. Payment will be withheld for each day at each intersection where the temporary signalization is not operational within 12 hours after notification.

102-13.19 Temporary Traffic Detection and Maintenance: Price and payment will constitute full compensation for furnishing, installing, operating, maintaining and removing temporary traffic detection including all equipment and components necessary to provide an acceptable signalized intersection. Take ownership of all equipment and components. Payment will be withheld for each day at each intersection where the temporary detection is not operational within 12 hours after notification.

102-13.20 Temporary Raised Rumble Strips: Price and payment will be full compensation for all work and materials described in this Section, including all cleaning and preparing of surfaces, disposal of all debris, furnishing of all materials, application, curing, removal, reinstalling and protection of all items, protection of traffic, furnishing of all tools, machines and equipment, and all incidentals necessary to complete the work.

102-13.21 Work Zone Pavement Markings: Price and payment will be full compensation for all work specified including, all cleaning and preparing of surfaces, furnishing of all materials, application, curing and protection of all items, protection of traffic, furnishing of all tools, machines and equipment, and all incidentals necessary to complete the work. Final payment will be withheld until all deficiencies are corrected.

Removable tape may be substituted for work zone paint at no additional cost to the Department.

Payment for temporary RPMs used to supplement line markings will be paid for under temporary retroreflective pavement markers. Install these markers as detailed in the Design Standards.

102-13.22 Temporary Lane Separator: Price and payment will be full compensation for all work specified in this Section.

102-13.23 Necessary Maintenance Services (Straight Time):  This pay item shall be used when using labor on Monday through Thursday. The contractor will be required and compensated for providing only one person to maintain the devices, unless otherwise directed by the Engineer.

102-13.24 Necessary Maintenance Services (Over Time): This pay item shall be used when using labor on Fridays through Sunday and holidays.  The contractor will be required and compensated for providing only one person to maintain the devices, unless otherwise directed by the Engineer.

102-13.25 Emergency Maintenance of Traffic: The contractor will be compensated for one Maintenance of Traffic pay item per work document. This pay will only be used when a work order is issued with a start date of less than 72 hours. This will be the only instance the Maintenance of Traffic (E102  1  2 ) pay item will be used.

102-13.26 Off Duty Law Enforcement Officer: The contractor will be compensated per hour as stipulated by the Engineer in the work document.

102-13.27 Truck Mounted Attenuator: All cost will be considered incidental to the pay item listed in the bid price proposal. Costs include operator.

102-13.28 When No Separate Item is Shown in the Proposal: When the proposal does not include a separate pay item for Maintenance of Traffic, all work and incidental costs specified as being covered under this Section will be included in the contract unit price for the work being performed and no separate payment will be made.

102-13.29 Partial Payment: When the proposal includes a separate pay item for Maintenance of Traffic - Lump Sum, partial payment will be prorated based on the percentage of contract amount earned for work completed and accepted by the Department.

102-13.30 Payment Items: Payment will be made under the items specified in the Bid Price Proposal.