## CONCRETE GUTTER, CURB ELEMENTS AND TRAFFIC SEPARATORS.

(REV 9-17-09) (1-13)

ARTICLE 520-1 (Page 671) is expanded as follows:

Construct or reconstruct in accordance with these specifications and in conformity with the existing conditions or the lines, grades, dimensions and notes shown in the plans and/or current edition of the Department’s Design Standards.

ARTICLE 520-2 (Page 671) is expanded by the addition of the following new Subarticle:

520-2.4 Weather: Assume all risk when placing concrete under adverse weather conditions. Permission from the Engineer to place concrete under such conditions will in no way relieve the Contractor of the responsibility of satisfactory results.

ARTICLE 520-7 (Page 672) is expanded by the addition of the following new Subarticle:

520-7.3 Clean-up: Remove from the job site any surplus or discarded materials or rubbish and restore the job site area to a condition acceptable to the Engineer, upon completion of work, and before final payment is made.  Disposal of concrete rubble, unless otherwise specified in writing by the Engineer, will be included in the contract unit price.

SUBARTICLE 520-12.6 (Page 673) is deleted and the following substituted:

520-12.6 Payment Items: Payment will be made under the items specified in the Bid Price Proposal.