## fencing.

(REV 9-18-09) (1-13)

Article 550-1 (Page 718) is expanded as follows:

Remove and replace damaged, destroyed, or deteriorated post and fence sections meeting the requirements of the Department’s Design Standards, and revisions thereto, current at the time of contract letting. Such work may include the removal of existing fence, removal of any public or private attachments to existing fencing, fence maintenance, furnishing of materials, replacement or mending of wire fabric, barbed wire, line post, corner and pull end post, braces, fasteners, other hardware, and gates.

Subarticle 550-3.1 (Page 718) is expanded as follows:

For repair of existing fence fabric, Type A, the use of Number 11 Farm, Design Number 1047-6-11, will be permitted, with Class 3 zinc coating meeting requirements of ASTM A 116.

Subarticle 550-4.1 (Page 719) is expanded as follows:

Unless otherwise specified, install replacement fence on the same alignment as the removed fence.

In cases where the fence is located along a limited access facility, perform the work in a manner that would maintain limited accessibility to the facility.

Replace all fence removed with replacement fence, or with temporary fence until the replacement fence may be installed, during any one working day.

Remove and provide disposal locations for all debris, including the original fence materials, from the right-of-way, at no additional cost to the Department. Remove all debris from the Department’s right-of-way at the end of each working day.

Article 550-4 (Page 719 - 720) is expanded by the addition of the following new Subarticles:

550-4.8 Gates: Install gates at locations specified in the work document issued by the Engineer. Install the manufacturer’s standard gate for use with the type of fence being installed.

550-4.9 Fence Maintenance: Perform miscellaneous activities such as, straightening, tightening and re-stapling or tying of existing fence as required.

Article 550-5 (Page 720) is deleted and the following Subarticles substituted:

550-5 Method of Measurement.

550-5.1 General: The quantities to be paid for will be the number of gates, the length of each type of fence, the number of corner post assemblies, and the number of pull and end post assemblies constructed and accepted.

550-5.2 Measurement of Fence Length and Payment: The length of fence to be paid for will be measured along the bottom of the fabric, out-to-out of end posts, in the completed and accepted fence. Measurement for Resetting Fence will be the actual length of existing fence reset.

Subarticle 550-6.1 (Page 720) is expanded by the following new paragraph:

(g) The removal cost of existing fence and components will be incidental to the cost of the new fence and components.

Subarticle 550-6.4 (Page 721) is deleted and the following substituted:

550-6.4 Payment Items: Payment will be made under the items specified in the Bid Price Proposal.