## highway lighting system (performance).

(REV 9-22-09) (1-13)

PAGE 864. The following is a new Section added at the end of Section:

SECTION ME715-50
HIGHWAY LIGHTING SYSTEM (PERFORMANCE)

ME715-50-1 Description.

The highway lighting system consists of overhead, underdeck, sign and navigational lighting.  Maintain the highway lighting system with a minimum of ninety percent (90%) of highway lighting (including Overhead, Underdeck and Sign Lighting) operational and one hundred percent (100 %) of Navigational Lighting operational as describes below in ME715-50.2.2.ME715-50-2 Requirements.

ME715-50-2.1 General: Possess a license to do business as a certified or registered electrical contractor pursuant to Chapter 489, Part II, Florida Statutes. Submit a copy of the license with the bid proposal package. All work is to be supervised by an onsite Journeyman Electrician possessing a current license from the local municipality or county.

Comply with all local licensing requirements and ordinances governing performance of the work. Perform all work in accordance with the laws of the State, all municipal ordinances, all regulations and requirements of the Public Service Commission, the National Electrical Code, the National Electrical Safety Code, the current edition of the Manual of Uniform Traffic Control Devices, the Florida Department of Transportation Design Standards for Design, Construction, Maintenance and Utility Operations on the State Highway System current at the time of the contract letting, and Department Standard Specifications.  Employees will be familiar with and apply all appropriate safety practices during the life of this Contract.  Training in the application of “Occupational Safety and Health Standards” (reference 29 of the Code of Federal Regulations, Part 1910.333) relating to “lockout and tagging” procedures will be MANDATORY for all persons employed on this Contract.

Immediately report to the Engineer any fatalities or serious injuries to either employees or members of the public and any extensive damage to property occurring during the performance of any of the work.

When substitutions are proposed for existing systems, they must be both functionally and aesthetically compatible with the existing components.

Maintain storage sites outside the right-of-way limits on any state maintained highway. Materials may be temporarily stored on the right-of-way outside of the clear recovery zone (excluding medians) for a period not to exceed twenty-four (24)-hours, if approved by the Engineer.

Adhere to the requirements of “Occupational Safety and Health Standards” (reference 29 of the Code of Federal Regulations, Part 1910), “Mobile and Locomotive Cranes” (American Society Mechanical Engineers International, ASME B30.5), and “Vehicle Mounted Elevating and Rotating Devices” (American National Standards Institute ANSI/SIA A92.2) for items relating to lifting devices (cranes, etc.).

ME715-50-2.2 Navigational Lighting: Navigational lighting outages that cannot be repaired within one (1) hour, during the periods when navigational lights are to be in operation, will require placement of temporary navigational lights until permanent repairs can be completed. Permanent repairs to any navigational lighting must be repaired within twenty-four (24) - hours.

ME715-50-2.3 Salvaged Materials: All replaced poles and parts will remain the property of the Department, unless determined by the Engineer to have no salvage value. Deliver all salvageable materials to storage sites identified by the Engineer. Dispose of all material in accordance with applicable Federal, State and local regulations. Provide documentation verifying proper disposal of all components removed containing mercury or other hazardous material.

ME715-50-2.4 Emergency Work: Be responsible at all times, including after normal work hours and weekends, for the immediate removal of downed poles or mast arms impeding traffic or threatening the public. Take immediate action to protect the safety of the traveling public by removing any elements of the pole assembly that may cause a hazard.

Replace light poles damaged by traffic within five (5) working days or within seven (7) working days if new foundations are required.  Take immediate action to protect the safety of the traveling public by removing any elements of the pole assembly that may cause a hazard.

Repair the electrical system in a way that prevents electrical shock to the public, the Department’s and Contractor’s work force.  Secure or replace any inspection plate, access panel cover or pull box cover that is not properly secured in place, damaged or missing.

Provide a contact person twenty-four (24)-hours-per-day and seven (7)-days-per-week including all holidays, for the duration of this Contract, to receive and respond to verbal and written work directions. This person will be required to respond, either in person or by telephone, within fifteen (15) minutes of being called or paged, and to report to emergency work site location(s) within one (1) hour after being notified.

ME715-50-3 Performance Measures.

The Department may perform highway lighting system inspections (Review of five (5) percent of the lighting, and a minimum of ten (10) for each cost center).  The following performance measures will be used in determining the reduction to each monthly invoice. If, in any Department inspection, the performance measures are not met.

| If the overhead, underdeck or sign lighting outage (individually or combined) exceeds ten percent (10%). | Reduction of $5000.00 per cost center. |
| --- | --- |
| For periods in excess of two (2) hour when navigational lights (either permanent or temporary lights) are nonfunctional, during times when navigational lights should be in operation, following notification. | Reduction of $100.00 per hour or portion thereof, per bridge, reduction per cost center. |
| If any inspection plate, access panel cover or pull box cover is found to be damaged, not secured, or missing | Reduction of $250.00, each occurrence per cost center. |
| If it is determined that the Contractor does not respond to an emergency site within one (1) hour of initial notification. | Reduction of $1000.00 per hour past the allowed response time or portion thereof, per incident per cost center. |

ME715-50-4 Basis of Payment.

Price and payment will be full compensation for all work and costs specified under this section. Payment will be based upon the lump sum price divided into sixty (60) equal monthly payments.

Payment will be made under the item specified in the Bid Price Proposal.