## Slide 1: E-bike Safety
What you need to know
E-Bike Safety Campaign
Notes: Welcome! Today we're talking about e-bikes. They're fun, fast, and a great way to get around, but they're also a big responsibility. It's important to know how to ride smart, stay safe, and avoid mistakes that put riders in the ER every year. Messaging themes: - Include the perks and fun and "cool" parts of e-bikes and riding. - E-bikes are awesome tools that can help you hang out with friends, get to school, a job, or sports, and be fun recreationally. - They are also a big step and responsibility. Your safety is in your hands whenever you are on any kind of device, and an e-bike is no different. - Level with the audience. They're growing up and you want to respect that. Having a mature, fun tone is a big part of connecting and getting that message home. - It's a conversation, not a lecture. Tip: Prior to the presentation, work with the school to have students submit anonymous questions. Teens may not want to ask questions in front of others. This could be done via pen and paper, Menti, or other survey mechanism (check phone policy).

## Slide 2: Why Ride an E-bike?
Independence: Get to school, work, practice, or a friend's house on your own schedule.
Practical: Carry gear, beat the heat, show up on time.
Speed & Fun: Faster than pedaling, no driver's license required.
Social: Ride with friends, explore your neighborhood.
But with great speed comes great responsibility.
Notes: [INTERACTIVE - 2 minutes] Raise your hand if you'd choose an e-bike over walking or waiting for a ride. Then ask why. Possible answers: being on time, not having a car, too hot for other types of travel, fun and easy. Ask: "What do you ride?" (e-bike, bike, scooter, hoverboard, skateboard, rollerblades, moped) Ask: "Where are you going when you ride?" (job, friends, sports, school, recreation) E-bikes are quicker than pedaling, they give independence, and you can ride with friends, all without a driver's license. But just because you don't need a license doesn't mean there aren't rules and responsibilities.

## Slide 3: Anatomy of an E-bike
Throttle
Seat
Center Column
Battery
Taillight
Headlight
Motor
Gears
Pedal Assist Sensor
Spokes
Disc Brakes
Controller/ Battery Mount
LCD Display
Handlebar
Pedal
Notes: Knowing the parts and pieces of your e-bike is key to being a responsible rider and keeping rides safe and fun.
E-bikes have more power and therefore more parts.
Maintenance, safety checks, and security are all part of responsible e-bike ownership.
Make sure to keep the manufacturer’s handbook and become familiar with your bike.
Activity:
Given all that, who thinks they can name all the parts accurately? E-bikes share a lot of commonalities with bikes, so some parts may be familiar – like pedals and wheels.
Image Source: https://www.towerelectricbikes.com/blogs/pages/ebike-electrical-system?srsltid=AfmBOorry8AHhIgwrMkJeYeWTuk3te_bCSU3xmfBm-rCiVKMy4XWfUNS

## Slide 4: What is a Legal E-bike?
Legal Requirements
2 or 3 wheels
Fully operable pedals
Seat or saddle
Electric motor: less than 750 watts
Manufacturer label with e-bike class
E-bike Classes
Class 1 — Pedal-assist only, up to 20 mph
Class 2 — Throttle-powered, up to 20 mph
Class 3 — Pedal-assist, up to 28 mph
If it exceeds 749 watts, has no pedals, or goes over 28 mph, it's not an e-bike. It's a motor vehicle.
Notes: [2 minutes] A legal e-bike must have 2–3 wheels, working pedals, a seat or saddle, and an electric motor under 750 watts. They must also have a manufacturer label indicating the class. While they may look alike, e-bikes come in different classes based on how the motor works and the top assisted speed: - Class 1: You pedal, the motor helps. Won't move without pedaling. Up to 20 mph. - Class 2: You press the throttle, the motor moves the bike. No pedaling needed. Up to 20 mph. - Class 3: You pedal, the motor gives a stronger boost. Up to 28 mph. Ask: "For those of you with an e-bike, do you know what class you have?" Important: If it's faster than 28 mph, over 749 watts, or has no pedals, it's no longer an e-bike. It's a motor vehicle. That means licenses, registration, and even insurance. Source: Florida Statute 316.003(4)

## Slide 5: Know Your E-bike!
Key Components
Motor & Battery The power source. Know your wattage and range.
Throttle & Pedal Assist How you control speed and power delivery.
Disc Brakes Most e-bikes use hydraulic disc brakes. They are very sensitive.
LCD Display Shows speed, battery level, and assist mode.
Lights Headlight and taillight. Required by law between dusk and dawn.
Mounting Safely
Motor disengaged
Battery on, assist set to zero
Hold the brake
Straddle the bike first
Then turn on assist
Warning: If you touch the throttle or pedal before you're ready, the bike can lurch forward.
Notes: [2 minutes] Knowing the parts and pieces of your e-bike is key to being a responsible rider and keeping rides safe and fun. E-bikes have more power and therefore more parts than traditional bicycles. Walk through the key components on the left. If you have a physical e-bike available for demo, this is a great time to point out the parts. For mounting safely: E-bike motors deliver significant torque from a standstill, so following a consistent startup routine prevents accidental lurches. The steps on the slide give you a reliable habit to build before every ride. Activity idea: Bring an e-bike or regular bike in for a demo. Ask students to identify parts.

## Slide 6: Before Every Ride…
The ABC-E Quick Check
A
Air — Inflate tires to max-rated PSI (check tire sidewall).
B
Brakes — Test both brakes. Lever should not reach the handlebar.
C
Chain — Moves freely, no rust, lightly oiled.
E
Electric — Battery charged, wiring intact, lights working.
Charging Safety
Use the original charger only
Charge on a flat, dry, hard surface
Never charge outside or on carpet
Unplug when fully charged
Inspect battery and wiring for wear, damage, or overheating
Lithium batteries can be dangerous if not properly stored. Safe charging prevents fires.
Notes: [2 minutes] We've covered your bike's anatomy. Now let's talk about checking it before each ride using the ABC-E Quick Check. (The ABC Quick Check is a standard pre-ride inspection used across bicycle safety education; the "E" for Electric has been added for e-bike-specific components.) A – Air: Check the air in your tires. They should be inflated to the max-rated PSI. Ask: "Does anyone know where to find the recommended PSI?" (Answer: the side of the tire) B – Brakes: Test both brakes. When you push the bike forward, the brakes should stop it. The lever should stop short of reaching the handlebar when pulled. C – Chain: The chain should move freely, be free of rust, and slightly oiled. E – Electric: Check the battery, any visible wiring or ports, and the lights. For charging safety: Most e-bikes and e-scooters use lithium batteries, which can be dangerous if not properly stored. Ask: "Do you charge your phone in the sun? Near water? When the cable looks damaged?" Same rules apply to your e-bike, but with more power behind it. Activity idea: Bring an e-bike in for an ABC-E demo.

## Slide 7: Gear Up: Protect Your Head
~69%
reduction in serious head injury risk when wearing a helmet
60%
of all bicycle-related deaths involve head injuries
The 2-V-2 Fit Check
2 fingers above your eyebrows
V shape of straps around each ear
2 fingers between strap and chin
Florida Law
Under 16? You MUST wear a helmet.
No helmet = a citation.
E-bikes are faster than traditional bikes. Consider a full-coverage or reinforced helmet for extra protection.
Source: National Safety Council; U.S. Consumer Product Safety Commission
Notes: [2 minutes] Your brain is the most precious cargo you carry. Protect it. A good helmet can prevent serious injury. Stats to emphasize: - Head injuries account for more than 60% of all bicycle-related deaths - Bicycle helmets reduce the risk of serious head injury by about 69%. - Fewer than half of adult cyclists regularly wear a helmet. Acknowledge the "dorky" factor: "I know that helmets may seem uncool sometimes. They can mess up your hair, get a little hot, and may not match your outfit. BUT they are just as important as seatbelts in a car." Walk through the 2-V-2 fit check. If you're still growing or change hairstyles, this is a great way to make sure your helmet still fits properly. Florida law: If you're under 16, you MUST wear one. No helmet = a citation. E-bike specific: Because e-bikes are faster than traditional bikes, consider a full-coverage or reinforced helmet with chin guard and eye shield. They even look cooler than traditional helmets! Activity idea: Bring helmets for proper fitting and walk through it with a willing volunteer. Source: National Safety Council; Florida Statute 316.2065

## Slide 8: Gear Up: Be Seen
If drivers can't see you, they can't avoid you.
Lights (Required by Law)
White light on front
Red light + reflector on rear
Required between dusk and dawn
Keep backup lights on your bike
Reflective Gear
Reflective tape or stickers on clothing
Reflective bands on arms or ankles
Retro-reflective materials visible from 600+ ft
Even if you skip the vest, add stickers
Bright Clothing
Light and bright colors are more visible
Dark clothing blends into the road at night
The farther away a driver sees you, the more time they have to react
Notes: [2 minutes] Ask: "Who here has biked or walked somewhere in the dark?" Where were they headed? By law in Florida, e-bikes operated between dusk and dawn must have a white front light and a rear red light and red reflector. Key message: If drivers can't see you, they can't avoid you. High-vis gear is just as important as a helmet. Even if you don't want to wear a vis-vest, getting reflective stickers or tape for your clothing can increase your visibility without feeling like a crossing guard. What time of year is this most important? Answer: winter, when the days are shorter. Prop ideas: Bike lights and reflectors to give out; retro-reflective sticker giveaways; demonstration in a dark room with bike lights and reflectors. Source: Florida Statute 316.2065; FHWA Visibility Education materials

## Slide 9: Where Can E-bikes Ride?
E-bikes have the same rights and rules as bicycles under Florida law.
Roads
Same rights and duties as a car.
Ride on the right side.
Use signals for turns.
Follow all traffic signs and lights.
Shared-Use Paths
Great when not crowded.
Announce before passing.
Remember: first come, first served.
Always pass respectfully.
Sidewalks
Pedestrians have priority.
Slow way down or walk your bike.
Not safe for e-bike speeds.
Must stop at every driveway and intersection.
Bike Lanes
Your designated space.
Can leave to avoid hazards or prepare for left turn.
Stay out of the door zone (5 ft from parked cars).
Notes: [2 minutes] Ask: "Where do you think an e-bike can ride?" Wait for answers. E-bikes have the same rights and rules as bicycles under Florida law, meaning they can ride anywhere bicycles ride. Some places may have slightly different local rules, so check before you head out. Key messages for each location: - Bike Lanes: Your space, but stay out of the door zone. You can leave the bike lane to avoid hazards. - Roads: You have the same rights AND duties as a car. That means stop signs, red lights, speed limits, and signals. - Sidewalks: Pedestrians always have priority. Most sidewalks are NOT appropriate for e-bike speeds. You cross car paths at every intersection and driveway. - Shared-Use Paths: Great when not crowded. When they are crowded, slow down and be respectful. If you aren't sure where you can ride, stick to roads, bike lanes, and bike paths. Local governments may require age minimums and/or government-issued photo ID for e-bike riders. Source: Florida Statute 316.2065

## Slide 10: Rules of the Road
When you're on the road, you're expected to behave like a vehicle.
1
Ride on the right side of the road
Never ride facing traffic. No one is looking for you from the wrong direction.
2
Signal your turns
Look, signal, and look again. Make eye contact with drivers.
3
Yield to pedestrians
They have priority in crosswalks and on sidewalks.
4
Use your lights
White front, red rear. Required between dusk and dawn.
5
Stop at all stop signs and red lights
Bicyclists must follow traffic controls just like cars.
6
Position for your destination
Turning right? Move right. Turning left? Move to the left side of the lane.
Notes: [2 minutes] When e-bikes are on roadways, with or without a bike lane, they are expected to follow the rules of the road and "behave" like a car. Being predictable, as we'll talk about more in a moment. These basic traffic principles apply whether or not there are signs, signals, or painted lines. They keep every road user, whether driving, biking, or walking, predictable to one another. Walk through each rule: 1. Ride on the right: Never ride facing traffic on road, bike lane, or shoulder. No one is looking for you from the wrong direction. 2. Stop at stops and lights: Just like a car. Must also obey pedestrian signals if present. 3. Signal your turns: Look over your shoulder (tuck your chin), signal, then look again before executing. 4. Position for destination: Right turn = right side. Left turn = left side of lane. 5. Yield to pedestrians: They always have priority in crosswalks. 6. Use your lights: Florida law requires lights between dusk and dawn. Optional activity: Act out each signal and ask the students to identify it correctly.

## Slide 11: Predictability is Safety
So is Defensive Riding.
These are the ONLY parts of riding you have 100% control over.
Notes: [1 minute - transition slide] "Alright, let's hit pause for a second. I know e-bikes are fast, and yeah, they're fun. But this part is important." There are two things that can make the difference between a safe ride and a tragic one: 1. Be predictable. 2. Ride defensively. These are the ONLY parts of riding you have 100% control over. You can't control the car behind you. You can't control a driver who's distracted. But you can control how predictable you are and how defensively you ride. That's all on you. Ask: "Who can give me an example of being predictable on a bike?" Ask: "And how about defensive riding?" When we say predictable, we mean: using signals, not swerving in and out of lanes, following road signs, making eye contact with drivers. Defensive riding is about: always scanning the road ahead and around you, assuming drivers don't see you (because sometimes they really don't), and watching for blind spots.

## Slide 12: Ride Defensively
1
Scan for hazards
Stay clear of road edges, potholes, and debris. Keep at least 5 feet from parked cars.
2
Don’t assume drivers see you
Wear bright or reflective gear. Use lights. Make yourself seen.
3
Keep your space
A driver can look right at you and still misjudge your speed. Position yourself in the lane so they have to notice you.
4
Communicate
Maximize how far ahead you can see. If you can’t see far enough to stop for a surprise, slow down.
5
Control your speed
Hand signals, eye contact, and audible warnings. Signal your intentions before you act.
Notes: [3 minutes] Walk through five key habits of defensive riding. These are the core skills every rider should develop. 1. Scan for hazards: Stay away from road edges where holes, glass, and debris can cause crashes, and keep at least 5 feet from parked cars. Riding too close to the edge leaves you no safe escape route if something goes wrong, and swerving to dodge hazards makes you unpredictable to drivers. 2. Don’t assume drivers see you: High-vis clothing and lights help, but visibility alone isn’t enough. A driver can look directly at you and still not register you as a factor. They misjudge your speed or just don’t think you’ll get there that fast. Position yourself in the lane so they have to acknowledge you. 3. Keep your space: Your position in the lane determines how far ahead you can spot trouble. The farther into the lane you ride, the better your sight lines and the more room you have to react. At higher speeds, you need to be even more assertive about your lane position. 4. Communicate: Use hand signals for turns and stops. Make eye contact with drivers whenever possible, and if you’re unsure they’ve seen you, wave or call out. A bell or verbal “on your left” goes a long way on shared paths. 5. Control your speed: E-bikes are faster and heavier than regular bikes, which means longer stopping distances. If you can’t see far enough ahead to stop in time, slow down. Brake before turns, intersections, and crowded areas. Your front brake provides the majority of your stopping power, so learn to use both brakes together.

## Slide 13: Speed Check: Brake Before You Have To
E-bikes are faster and heavier than regular bikes.
10 mph
29–39 ft
20 mph
71–111 ft
28 mph
114–194 ft
Most of your stopping power comes from the front brake. Learn to use both brakes together. Start braking earlier than you think you need to.
Distances include reaction time plus braking on dry pavement and vary with rider weight, brakes, and surface.
Distances based on standard traffic-engineering stopping-distance models (AASHTO parameters).
Notes: [3 minutes] This is one of the most important slides. E-bikes are significantly faster and heavier than traditional bikes, which means longer stopping distances and more force on impact. Weight comparison: - Standard bike: 20–40 lbs - E-bike: 40–80 lbs (2-4x heavier) - Average bicyclist speed: 12–15 mph - Class 1 & 2 e-bikes: up to 20 mph - Class 3 e-bikes: up to 28 mph The stopping distances shown account for perception-reaction time, the roughly 1 to 2.5 seconds it takes to spot a hazard, decide what to do, and begin braking. The exact time depends on how alert the rider is and whether they anticipated the conflict. Ask: "Does anyone know why 2.5 seconds is such an important number?" 2.5 seconds is the standard Perception-Reaction Time (PRT). Even if you hit the brakes immediately, your bike keeps moving during that time. Braking fundamentals: - Your front brake provides the majority of your stopping power, so learning to use it confidently is essential - Grabbing the front brake too hard without shifting your weight back can pitch you forward - Relying on the rear brake alone leads to skidding and significantly longer stops - Practice braking at low speed to get a feel for how responsive hydraulic disc brakes are - Good braking habits can cut your stopping distance significantly This slide corresponds to the "Speed Check: Brake Before You Have To" poster from the campaign materials. Distances based on standard traffic-engineering stopping-distance models (AASHTO parameters).

## Slide 14: Common Crash Types
Most crashes happen at intersections, caused by a driver failing to see or misjudging the speed of a bicyclist.
Right Hook
A driver passes you and turns right across your path before completing the pass.
How to avoid: Ride farther into the lane. Watch for cars slowing near turns. Be ready to brake.
Left Cross
A driver turning left thinks they can beat you through the intersection.
How to avoid: Move to a high-visibility position. Communicate for the driver to wait. Don't enter until sure.
Drive-Out
A driver pulling out from a driveway or side street can't see you.
How to avoid: Move left to be more visible. Slow down near driveways. If stopping distance > line of sight, slow down.
Dooring
A parked car's door opens in your path, throwing you into traffic.
How to avoid: NEVER ride within 5 feet of parked cars. Entirely avoidable with the right habits. Stay out of the door zone.
Notes: [3 minutes] Walk through each of the four most common crash types that e-bike riders should know about. RIGHT HOOK: The driver actually saw you when they started to pass, but they misjudged the time and distance needed to clear you before turning. This is about the driver not taking you seriously as a road user, not about them failing to see you. Countermeasure: Ride farther into the lane so drivers can't casually squeeze past. When a driver has to make a deliberate lane change to go around you, they're much more likely to wait until after the turn. LEFT CROSS: The driver turning left thinks they have time to get through before you arrive, or they can't see you behind other traffic. Countermeasure: Position yourself where the turning driver can see you clearly. Make eye contact or signal them to wait. Never enter an intersection if a left-turning driver hasn't clearly yielded to you. DRIVE-OUT: A driver pulling out of a driveway or side street may not be able to see you behind trees, hedges, or parked cars. Countermeasure: Shift left to make yourself more visible and to buy more reaction time. Slow down near driveways, especially if your view is blocked. DOORING: This crash is entirely avoidable with the right habits. Never ride within 5 feet of a parked or stopped car. A door opening into your path can throw you into the travel lane in front of overtaking traffic. Studies estimate dooring accounts for roughly 1 in 5 urban bike crashes. Key stat: Most cyclist injuries do NOT involve motor vehicles. Other cyclists, road hazards, and loss of control also cause crashes. But the ones involving cars tend to be the most serious. E-bike specific: Car drivers don't expect bikes traveling 20–28 mph. Their perception is that bikes are barely moving. This makes right hooks and sideswipes more likely.

## Slide 15: High-Risk Situations
NEVER ride alongside a large truck.
Truck drivers have massive blind spots. When trucks turn, the trailer sweeps across the lane and sidewalk. If a truck stops next to you at an intersection, dismount immediately and go to the sidewalk.
Door Zone
Stay 5+ feet from parked cars. Dooring is one of the most common urban bike crashes. If a bike lane is against parked cars with no buffer, ride outside the door zone.
Blinding Sun
When the sun is low on the horizon, drivers ahead may not see you. Oncoming drivers are looking directly into the glare and may not see you. Use a bright, flashing headlight.
Passing on the Right
All three intersection crash types can happen here. Don't pass a car unless you're sure it won't turn. Ride with caution and be ready to stop.
Notes: [2 minutes] TRUCKS - This is critical. Large trucks have extensive blind spots, particularly on the right side, and when they turn, the rear wheels track a much tighter path than the cab. That means the trailer can sweep across the bike lane, sidewalk, and curb area during a right turn. If you find yourself beside a truck at a red light: do not try to proceed when the light changes. Instead, step off your bike and move to the sidewalk until the truck has cleared the intersection. This is one of the most dangerous situations for any cyclist, and the safest response is simply to get out of the way. DOOR ZONE: Maintain at least 5 feet from parked cars at all times. Dooring is one of the most common types of urban bike crashes, and it is entirely avoidable by staying out of the door zone. If a bike lane sits right against parked cars with no buffer, ride along the outer edge of the lane or in the travel lane. Your safety matters more than staying inside the paint. BLINDING SUN: Many drivers keep going at full speed even when they can barely see. When the sun is at your back, be aware that oncoming drivers are looking directly into it and may not spot you at all. A bright, flashing headlight can help cut through the glare. PASSING ON RIGHT: All three intersection crash types can happen when passing on the right. Don't pass a car unless you're absolutely sure it won't turn right.

## Slide 16: Pass Properly
Don’t weave between cars — parked or otherwise.
Stick to a straight line on the sidewalk or on the road.
Avoid the door zone.
“Take the lane” if need be.
Notes: [2 minutes]
Passing is one of the most common situations where e-bike riders get into trouble. The key rule: maintain a straight, predictable line.
Don't weave between parked cars. If you duck in and out of gaps between parked cars, drivers behind you lose sight of you. When you re-emerge into the lane, they may not expect you.
Stick to a straight line. Whether you're on the road or on a sidewalk, riding in a consistent, predictable path gives drivers and pedestrians time to see you and react.
Avoid the door zone. We've said it before: stay 5+ feet from parked cars. When passing a line of parked vehicles, hold your line outside the door zone rather than riding close and swerving out for each car.
"Take the lane" if needed. If the lane is too narrow for a car to safely pass you, ride in the center of the lane. This is legal and prevents dangerous squeeze passes. You can move right when it's safe for the car to go around.
Remember: predictability is your best protection. A driver who can anticipate your path is far less likely to hit you.
Source: Florida Statute 316.2065

## Slide 17: E-bike Etiquette
Sharing the Road & Path
Slow down and yield to people on foot
Walk your e-bike across crosswalks
Don't swerve or weave between people
Ring a bell or say "On your left" when passing
Pass respectfully with plenty of space
On sidewalks: pedestrians have priority. You are the guest.
Limit Distractions
Put your phone away
One earbud is legal, but wearing two is not
Don't race friends in traffic
Don't do wheelies or stunts
Lock it up: Use a high-quality lock. Lock the frame and both wheels to a fixed rack. Bring your battery with you. Park where you can see it.
Wheelies can
result in arrest,
bike confiscation,
and may lead to e-bikes getting
banned or age-restricted
for everyone.
Notes: [2 minutes] E-bike etiquette: Sidewalks are first and foremost for people on foot. If you ride there, you're the guest. Walk through the sharing points and then the distraction points. On distractions: Phones are a huge distraction. One earbud is technically legal but both is not recommended because you need to hear traffic and other riders. On wheelies: This is important. Stunts on public roads can result in a citation or arrest, your bike being confiscated, and could contribute to lawmakers restricting or banning e-bikes for everyone. Riding responsibly protects your access and everyone else's. Security quick tip: E-bikes aren't cheap. Think about how much it would bum you out to have your phone stolen. Lock up properly: frame + wheels to a fixed rack, bring the battery with you, park where you can see it. Props: Bell, horn for demonstration.

## Slide 18: Identify the Hazards
Let's put your knowledge to the test.
For each scenario, identify:
What kind of area is this?
What hazards do you see?
What are the consequences?
How would you avoid them on an e-bike?
Notes: [3 minutes - INTERACTIVE SECTION] This is the interactive hazard identification activity. Use Google Street View images from the local area (Orange County) or from the school's neighborhood if possible. Show 2–3 street view images and for each, ask: - What kind of area is this? Is there a lot of foot traffic? Is it high speed? Are there parked cars? - Point out some risks you see in the photo. - What are the consequences? How are they avoidable on a bike or e-bike? Example hazards to look for: - Pedestrians stepping into crosswalks - Construction zones - Parked cars (door zone) - Driveways and cross streets (drive-out risk) - Potholes and debris - Large trucks at intersections - Poor weather or visibility - High-speed roadways This activity works best with 2–3 images from different environments: a downtown area, a suburban road, and a school zone or campus. Note: The previous presentation used Google Street View images from Melbourne, FL. For Orange County deployment, consider sourcing images from local roads familiar to students.

## Slide 19: What Would You Do?
Scenario 1
A car door suddenly opens in front of you.
This is why we stay 5+ feet from parked cars. If you're already in the door zone, brake and swerve left if safe to do so.
Scenario 2
A large truck is beside you at a red light. The light turns green.
Do NOT proceed. Dismount and go to the sidewalk. The trailer could sweep across your path.
Scenario 3
You're riding at 20 mph and a car pulls out of a driveway.
At 20 mph, stopping takes 71–111 feet. Brake immediately. Next time, slow down near driveways.
Scenario 4
You're riding home from practice and it's getting dark.
Turn on your lights (required by law). Wear reflective gear. Ride predictably.
Notes: [2 minutes] Read each scenario aloud and give students a moment to think before revealing the answer. This is a great opportunity for discussion. Ask students to share their reasoning and listen to their ideas before providing the correct answer. Additional scenarios to use if time allows: - A pedestrian steps into a crosswalk without looking. - You're approaching a busy intersection. What should you do? - A car is passing you on a narrow street. What's the risk? - The sun is low on the horizon behind you. What's the danger?

## Slide 20: Numbers that can Save Your Life…
5ft
Minimum distance from parked cars
70%+
Stopping power from your front brake
2.5sec
Average perception-reaction time
~I in 5
Urban bike crashes caused by dooring
~69%
Serious head injury reduction with a helmet
194ft
Stopping distance at 28 mph (worst case)
Notes: [1 minute] Quick review of the key numbers. These are the critical stats that every rider should know. Go through each one briefly. Ask students if they remember where each number came from in the presentation. These numbers will also be on any follow-up materials (wallet cards, posters, etc.) that students receive.

## Slide 21: Ride Smart. Ride Safe.
Always wear a properly fitted helmet.
Run the ABC-E check before every ride.
Ride defensively: scan, communicate, and assume drivers may not see you.
Stay 5+ feet from parked cars to avoid dooring.
Know your stopping distance. Brake early.
Use lights and reflective gear, especially at dusk and dawn.
Never ride alongside large trucks.
Respect pedestrians. On sidewalks, you're the guest.
Lock your bike properly. Protect your investment.
Notes: [1 minute] Bring it all together. Today we've talked about the core things you can control as a rider: your knowledge, your gear, and your predictability and defensive riding. Those are your superpowers on the road. Read through the takeaways. These are the key points that, if every rider followed them, would dramatically reduce crashes and injuries. Being safe isn't about slowing down your fun. It's about keeping you riding longer, with fewer crashes, and giving yourself the confidence to enjoy every ride.

## Slide 22: Questions?
What's one thing you'll do
differently next time you ride?
Ride smart. Be predictable. Stay defensive. Have fun.
E-Bike Safety Campaign
FDOT
Notes: [2 minutes] Engagement ideas for closing: - What's one thing you'll do differently next time you ride? - What's something new you learned today? - Any questions about what we covered? Scenario activity (if time allows): "I'll describe a situation, and you tell me how you'd handle it safely." - Approaching a busy intersection - A car door opens suddenly - A pedestrian steps into a crosswalk without looking - Riding home from an event in the evening End on a positive, empowering note: "Ride smart, be predictable, stay defensive, and have fun. You get to be independent when you ride, and that also means being responsible and safe." Optional: Share a personal story about a time you didn't follow road rules or safety and learned from it. Distribute any giveaway items: reflective bands, stickers, spoke cards, etc.