## Slide 1
FHWA’s Project-Level Safe System Alignment Framework and Tool
FHWA Resource Center
Elliott Moore

## Slide 2
The Safe System Approach
Image Source: FHWA
Notes: Key Message: This graphic presents an overview of the Safe System approach. There are three key components to understand, which will be explained on this and the following slides. These are the Safe System “approach,” “principles,” and “elements.” The Safe System “approach,” shown by the graphic on this slide, is the broadest term and describes all aspects of the Safe System.
In addition, the term “Safe System” is singular to depict an overall Safe Road System. The National Safety Council and our international partners also use this version.
Interactivity: No interactivity for this slide.
Background: This graphic was created for FHWA drawing inspiration from similar designs by the Institute of Transportation Engineers (ITE), the Road to Zero Coalition, and the Royal Society for the Prevention of Accidents (ROSPA) in the United Kingdom.
Notes: No notes for this slide.

## Slide 3
The “Swiss Cheese Model” of redundancy creates layers of protection
Death and serious injuries only happen when all layers fail
Post-crash care
Safe roads
Safe speeds
Safe vehicles
Safe road users
Post-crash care
Safe roads
Safe speeds
Safe vehicles
Safe road users
Image Source: FHWA
Adapted from James Reason’s model for analyzing accident causation
https://royalsocietypublishing.org/doi/10.1098/rstb.1990.0090
Swiss Cheese Model
Notes: A great way to visualize these “layers of protections” is to look at them through the Swiss Cheese Model.
Layered slices of swiss cheese (each with holes representing weaknesses) represent the individual elements of the “System”.
The basic principle is that lapses and weaknesses in one part of the system can occur (CLICK), but other parts compensate to not allow a failure (that is, a fatal crash).
A “failure” (CLICK) only results when a hole in each slice momentarily aligns (CLICK), permitting an incident to pass through holes in all the slices.
(Next Slide)
The “Swiss Cheese Model” is applicable to numerous risk management fields and was originally propounded by Dante Orlandella and James T. Reason of the University of Manchester

## Slide 4
The Safe System Approach is “Principles Based”
Achieving a Safe System requires all five elements to be strengthened
Safe Roads is a continuum, not an absolute
Top 3 Safe System “Takeaways”
Notes: Not an infrastructure initiative. If you get the principles, you’ll get it.
(CLICK)
There are 5 elements. Even though we’re only going to be talking about Safe Roads today, you need to strengthen all 5 Elements
(CLICK)
There are no “safe” or “unsafe” roads, but there are ways we can address the transportation system that can enhance the safety of its users. It’s not about eliminating risk, but REDUCING risk.
Key Message: The Safe System Approach is a complex topic and this presentation is an introduction. The top three things we want you to take away from this presentation are:
The Safe System Approach is “Principles Based” – you will learn the safe system principles that guide this approach and advance safety culture.
Achieving a Safe System requires all five elements to be strengthened – a system depends on each of its parts working together to achieve the best possible outcomes.
Safe Roads is a continuum, not an absolute – There are no “safe” or “unsafe” roads, but there are ways we can address the transportation system that can enhance the safety of its users.
Interactivity: No interactivity for this slide.
Background:

## Slide 5: “… implementing the Safe System Approach” What does that mean?
Different Thinking
Different Priorities
Different Decisions
Applying a Safe System Approach
Notes: It’s not the same thing we’ve always done. I
We have to do things differently.
It’s about managing Kinetic Energy such that we can eliminate FATAL and SERIOUS INJURY crashes… not all crashes

## Slide 6
Source: FHWA
https://highways.dot.gov/sites/fhwa.dot.gov/files/2024-01/Safe_System_Roadway_Design_Hierarchy.pdf
Advancing the Safe Roads Element in the SSA
Notes: The first part of this presentation is going to focus on the Safe System Roadway Design Hierarchy.
There are 5 elements, but we’re going to focus on the Safe Roads element.
Key Message: The five Safe System “elements,” highlighted in the middle ring of the graphic, are conduits through which the Safe System approach must be implemented. The key focus of the Safe System approach is to reduce death and serious injuries through design that accommodates human mistakes and injury tolerances. Making a commitment to zero deaths means addressing every aspect of crash risks through the five elements of a Safe System. These layers of protection and shared responsibility promote a holistic approach to safety across the entire roadway system. The five elements will be discussed in depth later in the presentation.
Interactivity: No interactivity for this slide.
Background: No background for this slide.
Notes: No notes for this slide.

## Slide 7
The Safe System Roadway Design Hierarchy is a tool that characterizes engineering and infrastructure-based countermeasures and strategies relative to their alignment with the Safe System Approach (SSA).
Safe System Roadway Design Hierarchy
Notes: Here is a QR code so you can download this free publication.

## Slide 8
Eliminate
Physically remove the hazard
Substitute
Replace the hazard with option that lowers severity
Engineering Controls
Operate the system to reduce exposure
Administrative Controls
Education, legislation & policies to change behavior
Personal Protective Equipment
PPE, protective gear
Adapted from National Institute for Occupational Safety and Health – https://www.cdc.gov/niosh/topics/hierarchy/default.html
Hierarchy of Controls
More Effective
Less Effective
The Safe System Roadway Design Hierarchy is emulated from the hierarchy of controls for workplace safety
Inspired by Occupational Safety
Notes: At FHWA, we focus a lot of our efforts on R&D… Rip-off and Duplicate!
As you can see from our occupational safety counterparts, they two operate on a hierarchy of controls to PREVENT workplace events.
Prevention through Design
Initiative led by the National Institute for Occupational Safety and Health (NIOSH) to prevent or reduce occupational injuries, illnesses, and fatalities through efforts that anticipate and “design out” hazards to workers.
Hierarchy of controls is a PtD strategy.
https://www.cdc.gov/niosh/topics/ptd/

## Slide 9
vision-zero-strategic-plan-120120.pdf (bellevuewa.gov)
vision-zero-strategic-plan-120120.pdf (bellevuewa.gov)
ELIMINATION
SUBSTITUTION
ENGINEERING
CONTROLS
ADMIN
CONTROLS
PPE
LEAST EFFECTIVE
MOST EFFECTIVE
Safeguard with Personal Protective Equipment.
Reflective Vests, Pedestrian Crossing Flags, Bicycle Helmets, Seatbelts, Airbags
Change the Way People Travel.
Education Campaigns, Marked Crosswalks, Pedestrian Crossing Buttons, Sharrows, Permissive Signal Phases, Signage
Isolate People from Traffic Conflicts.
Sidewalks, Protected Bikeways, Curbs, Bollards, Traffic Diverters, Pedestrian-Prioritized Signals, Speed Humps, Chicanes
Physically Remove Traffic Hazards.
Pedestrian Streets, Offstreet Paths, Scramble Crossings, Dedicated Transitways, Automated Speed Limiters
Replace with Lesser Hazards.
Home Zones, Shared Streets, Neighborhood Greenways, Roundabouts, Automated Speed Enforcement
Hierarchy of Street Safety Controls
Notes: But at FHWA, we were not the first to rip off this concept The City of Bellevue in WA created this hierarchy that has some similar components to what we’ll be exploring today.
Adapted from versions created by Cathy Tuttle and Queen Anne Greenways. Based on Recommendations of Hazard prevention and Control created by US Department of Labor Occupational Safety & Health Administration and the Center for Disease Control and Prevention. Effective controls protect people from workplace hazards; help avoid injuries; illnesses and incidents; minimize or eliminate safety and health risks; and help employers provide workers with safe and healthful working conditions and help prevent and control hazards.

## Slide 10: What’s Old is New
Delineate
Shield
Make Crashworthy
Make Traversable
Hierarchy to address hazards within the roadside clear zone
Derived from AASHTO Roadside Design Guide.
Remove
Source: FHWA
Notes: The idea of a hierarchy isn’t new in transportation design either. Do any of you have prior experience with the AASHTO RDG?

## Slide 11: Slide Title

## Slide 16: Protected Left Turn Signal Phasing
Consider:
Protected only left turn signal phasing; or
Flashing Yellow Arrow to omit permissive movement when there is a pedestrian call
“Permissive” left-turning vehicular traffic is a concerning risk that pedestrians and cyclists face at many signalized intersections
Notes: FL has too many Protected-permissive operations.
Give Mike example.
“that’s going to mess up our LOS” – we have to do things different… different priorities…

## Slide 17
Notes: It’s not that they’re not good, just not as affective

## Slide 18
Note: This figure is a simplified graphical representation of a concept and is not intended to imply a precise numerical relationship. The lack of units on this graph is intentional.
Existing Condition
“Safe Roads” is a Continuum – Not an Absolute
Notes: Shifting down a continuum.

## Slide 19
Complete Streets implementation may apply the Safe System Design Hierarchy to identify and prioritize safety enhancements.
Applying the Hierarchy to Implement
Complete Streets
Notes: Plug for complete streets. Tiers can help prioritize complete street improvements

## Slide 20
Safe System Alignment Frameworks (dot.gov)
Notes: This project-based is intended to be simpler… I was told there is no MATH.
CAN BE USED ON ROAD SEGMENTS.

## Slide 21: Background – International Perspectives
https://austroads.com.au/latest-news/safe-system-assessment-framework
“… designed to help road agencies methodically consider Safe System objectives in road infrastructure projects.”
Notes: R&D – ripped off and duplicated. Inspired by Australia
All FHWA does is R&D…
Exposure/Likelihood/Severity
Ours is more quantitative vs qualitative

## Slide 22
Notes: Spreadsheet tool screenshots
Overview

## Slide 23: Project-Based Alignment Framework
Project-Based Alignment Framework Factors
Source: FHWA.
Safe Speeds, Safe Roadways (Quantitative)
Crash Exposure
Crash Likelihood
Crash Severity
Safe Users, Safe Vehicles, Post-Crash Care (Qualitative)
Prompts and Questionnaires
Notes: Three legs of a stool
Exposure – traffic volumes, crossing distance, etc.
Likelihood – risk factors
Severity – primarily speed
High severity, but low exposure… maybe not as big of a concern…. Conversely, high exposure….

## Slide 24: Managing Expectations
Source: https://www.merriam-webster.com/dictionary/framework
Flexible structure ≠ Rigid adherence to defaults
Notes: Manage expectations… this is a framework… not end all be all
“Basic” structure
Framework is good… details can be flushed out later… framework is applicable to everyone
FL’s expectations for high volume vs Montana’s may be different… they can be changed based on your agency preference

## Slide 25
Score
Exposure
Likelihood
Severity
Project-Based Alignment Framework
Notes: These going into an SSA Score

## Slide 26: Exposure
The volume and/or length (distance) various users are using a facility and could be involved in a potential crash
Source: FHWA.

## Slide 27: Project-Based Alignment Framework: Exposure Scoring Matrix
Notes: Inputs
Tool does differentiate between VRUs and Motor vehicles.
You can adjust to conditions that fit your state/district/locality… but the concept is to keep these categories

## Slide 28: Likelihood
Elements and/or risks that impact the probability of a crash taking place by influencing the opportunity for conflict and/or user error rates
Source: FHWA.
Notes: Definition of likelihood

## Slide 29: Risk Factors – Motor Vehicles
Lighting Conditions
Fixed Objects
Right Turn on Red Conditions
Permissive Left Turns
Obstructed Sight Distance
Topography (grade)
Roadside Recovery Area
Roadside Drop Off
Rumble Strips
Right Turn Lane Channelization
Driveways
Separation of Opposing Traffic Movement
Crossing Conflicts
Intersection Skew
Road Curvature
The Framework Tool allows users to enter additional risk factors
Notes: These are the motor vehicle risk factors that are currently included
Can add additional

## Slide 30: Risk Factors – Pedestrians & Bicycles
Space Separation
Crosswalk Markings
Right Turn on Red Conditions
Permissive Left Turns
Bicycle Boxes
Separation in Time
Pedestrian Signal Phasing
Bicycle Signals
Lighting
Obstructed Sight Distance
Driveways
Topography (grade)
Free Flow Right Turns
Intersection Skew
Road Curvature
The Framework Tool allows users to enter additional risk factors

## Slide 31: Severity
Factors that impact the probability of a serious or fatal injury in the event of a crash
Source: FHWA.
Notes: Primarily speed

## Slide 32: Severity Scoring

## Slide 33: Alignment Scoring Matrix
Notes: Enter all of the data and you get a score… you can use it to compare alternatives… it’s all relative to the other alternatives.

## Slide 34: Reality Check
What do the scoring numbers mean?
  The scoring values are unitless and meant for comparison purposes only
For what purposes should I use this tool?
  Comparisons of current conditions to proposed improvements
  Comparisons of options and alternatives
Notes: Think about RSAs

## Slide 35: Application to Support Road Safety Audits
Road Safety Audits (RSA) | FHWA (dot.gov)
Application of Safe System Framework
Step 4 – Perform Field Reviews
Assess Framework Risk Factors
Step 5 – Analyze and Report on Findings
Quantitative Scores for Vulnerable Road Users and Motor Vehicles
Step 6 – Present Findings to Owner
Quantitative Comparison of Existing Conditions to RSA Suggestions

## Slide 36
Other Safe System Elements
Notes: Focuses on safer roads elements
Has Prompts in regards to the other SSA elements
You DON’T have to go through these… optional

## Slide 37
Other Safe System Elements

## Slide 38
Notes: Also has an equity prompt

## Slide 39
Regression-based models
Relies on past crash data
Context-based (rural/urban, functional class, segment/ intersection, etc.)
Local calibration is important
Does not rely on crash data
RSA-style, prompt-based series of questions
Framework allows for adjustments based on local conditions and priorities
Results characterized in numeric terms intended for relative comparison
Does not rely on crash data
Uses kinetic energy management model (KEMM)
Principles-based, not crash-based
Inputs, methodology are objective, numeric
Crash-Based Tools (HSM)
SSA Alignment Tool
Safe System Intersection (SSI) Analytical Method
Safety Analysis Toolbox
Notes: HSM is very data intensive – local calibration… statistics, math, applicability, etc.
SSA simple. Framework. Adjusted/flexible. Relative to project. However, still quantitative… EASY TO USE
SSI – math heavy… but does a better job quantifying FSI crashes (already in your SPICE V5 tool) – more robust

## Slide 40
Notes: Not going to get into this, but we do have a policy-based framework
Look at your existing policies to see how they align to SSA.
Mostly fluff
Broward County was one of pilot locations for applying this.

## Slide 41: Contact Us
Elliott Moore, PE
Senior Safety Engineer
FHWA Resource Center
elliott.moore@dot.gov
Mark Doctor, PE
Senior Safety & Design Engineer
FHWA Resource Center
mark.doctor@dot.gov