## Slide 1
Robert J. Potts
Senior Scientist
E Sciences, Incorporated
Statewide Spill Prevention, Containment, and Response Training

## Slide 2: Presentation Overview
Background
Regulatory Basis
Target Audience and Focus
Training Format
Training Content
  Spill Prevention
  Spill Containment
  Spill Reporting

## Slide 3: Statewide Spill Prevention, Containment, and Response Training
Background:
Spill Prevention Control and Countermeasure (SPCC) Plans or other Contingency Plans at Maintenance Yards or Operations Facilities with high volume fuel and oil storage containers.

## Slide 4: Statewide Spill Prevention, Containment, and Response Training
Background:
FDOT maintenance staff and contractors use petroleum products and other chemicals in daily activities.

## Slide 5: Statewide Spill Prevention, Containment, and Response Training
Regulatory Basis:
Part III.A.7(d) NPDES Phase I MS4 Permit
  The permittee shall continue to implement procedures to prevent, contain, and respond to spills that may discharge into the MS4.
  The training shall include how to prevent a spill, recognize and quickly assess the nature of a spill, contain a spill, and promptly report hazardous material and chemical spills to the appropriate authority.

## Slide 6: Statewide Spill Prevention, Containment, and Response Training
Target Audience and Focus:
FDOT field maintenance staff
FDOT maintenance contractors
Focus will be:
  Non-roadway spills
  Small spills at FDOT yards & operations facilities
  Spills that may occur in the field

## Slide 7: Statewide Spill Prevention, Containment, and Response Training
Training Format:
Similar to IDDE Training
Video
English and Spanish narration
Approximately 15 minutes in duration
Available via the web
Available as a CBT

## Slide 8: Statewide Spill Prevention, Containment, and Response Training
Training Content:
Spill Prevention
Spill Containment
Spill Response

## Slide 9: Statewide Spill Prevention, Containment, and Response Training
Spill Prevention:
Observations
  Report dangerous or unstable chemical storage or usage practices
  Strong chemical odors, burning eyes, staining, and or dead vegetation or animals
  Look for sharp objects along spray routes or travel corridors
  Replace worn or corroded storage containers

## Slide 10: Statewide Spill Prevention, Containment, and Response Training
Spill Prevention:
Best Practices
  Ensure containers are properly capped and sealed
  Store heavy chemical containers on lower shelf
  Replace leaking containers and hoses
  Limit exposure of chemical containers to the environment (sun, rain)
  Ensure effective secondary containment is present
  Identify and eliminate unsafe storage practices
  Be aware of surroundings and current activities

## Slide 11: Statewide Spill Prevention, Containment, and Response Training
Spill Containment:
When a spill occurs
  Stay calm!
  Ensure your safety and others in area first
    Remove any non-essential personnel from affected area
    Stop and or remove machinery and vehicles from area
  Notify supervisor

## Slide 12: Statewide Spill Prevention, Containment, and Response Training
Spill Containment:
Evaluate the Situation
  Safety first!
  Note wind direction – stay up wind of spill
  Identify the source of the spill
  Estimate size of impacted area
  Estimate volume of material spilled
  Is the spill spreading?

## Slide 13: Statewide Spill Prevention, Containment, and Response Training
Spill Containment:
Stop or limit spreading of spill:
  Safety first - proceed only if spilled substance is known!
  Put on proper personal protective equipment (PPEs)
  Secure area and limit access

## Slide 14: Statewide Spill Prevention, Containment, and Response Training
Spill Containment:
  Close valves
  Stand up tipped over drum, tank, or barrel
  Place absorbent materials
  Re-route spill away from inlets or drains
  Plug or patch hole in container

## Slide 15: Statewide Spill Prevention, Containment, and Response Training
Spill Response:
Small Spills
Large Spills
Major Spills

## Slide 16: Statewide Spill Prevention, Containment, and Response Training
Small Spills
  Generally less than 25 gallons
  Occurred on an impervious surface
  A known material
Large Spills
  Generally more than 25 but less than 100 gallons
  Occurred on soil or impervious surface
  A known material

## Slide 17: Statewide Spill Prevention, Containment, and Response Training
Major Spills
  Generally greater than 100 gallons
  Occurred on soil, into the storm sewer, or waterbody
  An unknown material

## Slide 18: Statewide Spill Prevention, Containment, and Response Training
Small Spill Response
  Initiate response only if it can be done safely
  Wear proper PPEs
  Place absorbents on spilled material
  Sweep up absorbents and spilled material
  Dispose of material properly
  Notify supervisor and District NPDES Coordinator

## Slide 19: Statewide Spill Prevention, Containment, and Response Training
Large Spill Response
  Follow response protocol
    Contact DCIC
    Contact District NPDES Coordinator
    Contact State Warning Point system
  Provide spill information
  Identity of spilled material
  Identify source of spilled material (if known)
  Estimated volume of release
  Location and access information where spill occurred

## Slide 20: Statewide Spill Prevention, Containment, and Response Training
Large Spill Response
  Control or contain spill if able to do so in safe manner
  Dike spill with absorbent material
  Trench spill to direct away from inlets or waterbody
  Secure area
  Wait for spill response/ clean up contractor

## Slide 21: Statewide Spill Prevention, Containment, and Response Training
Major Spill Response
  Follow response protocol
  Contact DCIC
  Contact District NPDES Coordinator
  Contact State Warning Point
  Provide spill information
  Identity of spilled material (if known)
  Identify spill source (if known)
  Estimated volume of release
  Location and access information where spill occurred
  Name of receiving water(s)
  Identify affected storm sewer inlets and pipe routes

## Slide 22: Statewide Spill Prevention, Containment, and Response Training
Major Spill Response
  Secure area
  Stop machinery and remove vehicles in area
  Wait for spill response / clean up contractor

## Slide 23: Statewide Spill Prevention, Containment, and Response Training
Hierarchy of Importance
Safety First!! For you and others in area
Minimize exposure by isolating area
  Re-route pedestrian traffic, if applicable
  Set up cones or barricades around affected area
Minimize environmental impacts
  Keep spilled material out of waters and storm sewers
Minimize clean up costs

## Slide 24
Questions / Comments?