## Slide 2: Webinar Staff
Gina Bonyani
Maria Overton
Karla Matos

## Slide 3: Agenda
How to Participate
Credits and Webinar Material
Introduction to Access Management
Questions
Contact Info

## Slide 4: How to Participate Today
Open and close your Panel
View, Select, and Test your audio
Submit text questions
Raise your hand
Q&A addressed throughout the webinar

## Slide 5
Tue, Aug, 27, 2019 | 2:00PM - 3:30PM EDT
Tue, Nov 12, 2019 | 2:00PM - 3:30PM EST
Tue, Feb 11, 2020 | 2:00PM - 3:30PM EST
Tue, May 12, 2020 | 2:00PM - 3:30PM EDT
The FDOT Access Management Webinar Series 2019-2020 have been scheduled for the following dates:
NEXT!

## Slide 6: Learning Curve
FDOT’s Systems Implementation Office is utilizing the Learning Curve system for participant communications and management of the Statewide Access Management Quarterly Webinar.

## Slide 7: Credits Information
Credits will be distributed four to five business days after the webinar, through Learning Curve.
  PDH’s Credits, AICP Credits Information, and Course Certificates
Your participation will be recorded by GoToWebinar.
  You will need to attend to the entire webinar with the unique link provided by GoToWebinar.

## Slide 8: Webinar Material
Webinar materials will be sent via the Learning Curve System.
Recorded webinars and presentation material will be posted on the Systems Implementation Office website:
  Training & Webinars
    Access Management

## Slide 9: Poll Questions

## Slide 10: What organization do you Represent?
FDOT
Local Government
Private Firm
Other

## Slide 11: How familiar are you with Access Management?
Very Familiar
Somewhat Familiar
Not Familiar

## Slide 12: Today’s Webinar
Introduction to Access Management
Tuesday, August 27, 2019
2:00PM – 3:30 PM, EDT
Credits: 1.5
Speaker:
Gina Bonyani, Transportation Planner | FDOT

## Slide 13: What is Access Management
Access management involves the location, spacing, and design of driveways, medians, median openings, traffic signals, and interchanges.
The roadway network must be viewed as a system of all the features mentioned above, not as one isolated element.

## Slide 14: Components
Driveways
Medians
Median openings
  Full access
  Directional
Signals
Interchanges
Driveways
Traffic Signals
Median Openings
Interchange Ramps

## Slide 18
1
2
3

## Slide 21: Why is Access Management Important?
Access management provides safe and efficient
transportation facilities for all roadway users

## Slide 22: Benefits
Access management helps to:
  Reduce conflicts
  Enhance safety
  Lessen severity of crashes
  Improve mobility
  Increase connectivity
  Develop aesthetics
As driveways increase, crashes increase
As driveways increase, capacity decreases

## Slide 23: Goals
Passenger cars
Pedestrians
Cyclists
Transit
Trucks

## Slide 26: Conflict Points
Full unsignalized median opening
HIGH CONFLICT

## Slide 27: Less Conflict Points
Directional median opening

## Slide 28: RCUT(Restricted Crossing U-Turn)

## Slide 29: Guiding Principles
Limit the number of conflict points
  Reduce the number of median openings
  Provide directional median openings
  Consolidate driveways to reduce frequency
Look at conflict points from a network perspective

## Slide 30
Raised median installation
Full median
opening

## Slide 31: Guiding Principles
Separate the conflict points for all modes of transportation
  Driveway spacing
  Median opening spacing
  Traffic signal spacing
  Distance of driveway/median opening/signal from interchange ramps

## Slide 32
DRIVEWAYS

## Slide 33
CONSOLIDATED DRIVEWAYS
Separating Conflict Points

## Slide 34: Site Circulation
Vehicular Queuing
  Existing Traffic Conditions
  Future Traffic Conditions

## Slide 35: Site Circulation
Vehicular Queuing
  Existing Traffic Conditions
  Future Traffic Conditions
Median Modification
  Eliminates main street left turn access
  Side street right in/right out

## Slide 36: Parking Restrictions

## Slide 37: Highway Safety Manual
Methodologies for predicting average crash frequency given certain roadway characteristics
Factors to be applied to reduce crashes

## Slide 38: Highway Safety Manual
Example: suburban 4-lane arterial at 45 mph
Divided with 10’ median
3.9 crashes/year/mile
Undivided (no median)
5.8 crashes/year/mile
Divided with driveways
4.9 crashes/year/mile
Undivided with driveways
11.5 crashes/year/mile

## Slide 39: Highway Safety Manual
Crash Modification Factors
  CMF is the percentage of crashes remaining after an improvement, i.e. 0.90 means 10% reduction in crashes
  Examples of factors for access management improvements:
Add Median CMF=0.75
25% fewer crashes
Widen Median 10ft. CMF=0.85
15% fewer crashes
Reduce Access Points CMF=0.70
30% fewer crashes
Install Signal CMF=0.75
25% fewer crashes

## Slide 40: What are the Access Management Standards?
The FDOT Access Management standards are established in Florida Administrative Code Chapter 14-97, otherwise known as Rule 14-97.
John McWilliams, South Florida

## Slide 41: Rule 14-97: Table 1
Access Management Standards for Limited Access Facilities
Access Class | Area Type | Segment Location | Interchange Spacing (MILES)
1 | Area Type 1 | CBD & CBD Fringe For Cities In Urbanized Areas | 1.0
 | Area Type 2 | Existing Urbanized Areas Other Than Area Type 1 | 2.0
 | Area Type 3 | Transitioning Urbanized Areas And Urban Areas Other Than Area Type 1 or 2 | 3.0
 | Area Type 4 | Rural Areas | 6.0

## Slide 42: Rule 14-97: Table 2
Access Class | Medians | Connection Spacing (FEET) |  | Median Opening Spacing (FEET) |  | Signal Spacing (FEET)
 |  | > 45 mph | ≤ 45 mph | Directional | Full | 
2 | Restrictive with Service Roads | 1320 | 660 | 1320 | 2640 | 2640
3 | Restrictive | 600 | 440 | 1320 | 2640 | 2640
4 | Non-Restrictive | 660 | 440 |  |  | 2640
5 | Restrictive | 440 | 245 | 660 | *2640/ 1320 | *2640/ 1320
6 | Non-Restrictive | 440 | 245 |  |  | 1320
7 | Both | 125 |  | 330 | 660 | 1320
Typically Undeveloped
Typically Developed
Access Management Standards for Arterials
*2640 feet for > 45 mph; 1320 feet for <45mph
“Restrictive”= Physically prevent vehicle crossing
“Non-Restrictive”= Allow turns across at any point

## Slide 43: Measuring Spacing
Signal Spacing
Directional Spacing
Full Spacing
Directional Spacing
Connection Spacing

## Slide 44: Right to Access
Must provide reasonable access to roadway
  What does “reasonable” mean?
  How is it defined?
  Does everyone get a driveway?
An owner has a right to property access but not a right to direct left turn.

## Slide 45: FDOT Procedures
Systems Implementation Office
Topic No. 625-010-021-h: Median Openings and Access Management
Under Review!
https://fms.fdot.gov/

## Slide 46: Procedures
Each district shall have an Access Management Review Committee (AMRC) to review deviations from spacing standards of more than 10%
The AMRC is appointed by the District Secretary and consists of head level positions (District Design Engineer, District Planning Manager, etc.) and meetings are given public notice
>10% Deviation
Review by AMRC

## Slide 47: Site B must be reviewed by AMRC
Site A
650 ft spacing
= 1.5% deviation
Site B
560 ft spacing
= 15% deviation

## Slide 48: Procedures
Avoid median openings
across left-turn lanes

## Slide 49: Procedures
Avoid median openings
across right-turn lanes

## Slide 50: Procedures
Avoid median openings
across recurring queues

## Slide 51: Procedures
Avoid median openings
within functional area of
signalized intersection

## Slide 52: Design criteria and Rules
FDM Chapter 214 provides driveway design criteria and requirements for connections to the State Highway System.
Florida Administrative Code (F.A.C.):
  Rule 14-96 (State Highway Connection Permits)
  Rule 14-97, F.A.C. (State Highway System Access Control Classification System and Access Management Standards).

## Slide 53: Access Management and Site Design
Successful access management involves more than regulation of median openings and driveways; it can also be achieved by thoughtful planning during the site design process and coordination with developers.

## Slide 54: Inter-Parcel Access
Inter-parcel access can be developed between adjacent parcels or large multi-use properties
  Improves connectivity
  Reduces number of driveways on major streets
  Enhances bicycle/pedestrian access

## Slide 55
1
2
3
4
5
6
Adjacent Development
Plaza

## Slide 56
One driveway serves Walgreens, McDonalds, and two service stations

## Slide 57
No driveways

## Slide 58
Unconnected development
entrances

## Slide 59
Leads to a unified development

## Slide 61: Concept Illustrations
Some examples of actual facilities with good design and some with only vehicles in mind.
Can you tell which is good and which is bad?

## Slide 62
Conflict Potential

## Slide 63
Driveway
Intersection

## Slide 67: Guides Being Combined
Median Handbook
Driveways Information Guide
Access Management Guidebook
DRAFT

## Slide 68: Resources
FDOT, Access Management Guidebook (Driveway and Median)
https://www.fdot.gov/planning/systems
Florida Design Manual
https://www.fdot.gov/roadway/fdm/default.shtm
FHWA Access Management
https://ops.fhwa.dot.gov/access_mgmt/index.htm

## Slide 69
Questions
Gina Bonyani
Transportation Planner- FDOT
Gina.Bonyani@dot.state.fl.us

## Slide 70: Course Details
Survey through GoToWebinar
FDOT FBPE Provider Number: 0003533
APA Course Web Page https://www.planning.org/events/eventsingle/9182414/
APA Course Number: 9182414
AICP/PDH Credits Provided: 1.50

## Slide 71: Contact Info
Gina.Bonyani@dot.state.fl.us
Maria.Overton@dot.state.fl.us
Karla.Matos@dot.state.fl.us