## Slide 1
Executive Workshop
April 15, 2020
STRIDES 2 Zero
(SAFE)
1
Notes: STRIDES 2 Zero
State Traffic Roadway and Intersection Data Evaluation System 2020
SAFE
System Analysis and Forecast Evaluation

## Slide 2: SAFE STRIDES 2 Zero Program
SAFE
System Analysis and Forecast Evaluation
STRIDES 2 Zero
State Traffic Roadway and Intersection Data Evaluation System 2020
SS2Z
SAFE STRIDES 2 Zero
Leverages various data sources to enhance safety & mobility of the state highway system (SHS)
Aligns with three of the four Vital Few Safety Initiatives
  Enhancing safety
  Improving mobility
  Inspiring innovation with a predictive method of analyzing safety data
Enhances roadway network screening
  Previous method: Hot-spot analysis
  SS2Z program: Quantitative evaluation with Florida specific crash predictive analytics tools
2
Notes: Question:
To the department, how valuable is it to identify intersections that have the most potential for safety improvements on an annual basis?
Use leading-edge scientific predictive methods to screen and identify candidate intersections that have the most potential for safety improvements.
Diagnose, identify and select engineering countermeasures that reduce fatal and severe injury crashes.

## Slide 3
Annual SAFE Reporting Overview
KA: Fatal and Severe Injuries
2020 SHS Signalized Intersection Candidates: 154 Sites
Chart: 
| Fatalities | Serious Injuries
SW 45 Fatalities and 173 Serious Injury | 0.11 | 0.89
$1.07 Billion Societal Savings Over 20-Year Design Life
$40.4 Million
Estimated Construction Cost:
Safety Benefit per Year:
$78.5 Million
5
SAFE Implementation:
Less Fatalities Per Year
24% Reduction of the Trend
11%
Serious Injuries
89%
349
Total Observed KA Crashes per Year for Candidates:
SHS Signalized Intersection
7-year Safety Trend:
21
Fatalities Per Year Increased
Fatalities
16%
KA Crash Reduction with
SAFE Implementation:
Notes: NPV = 1.07 Billion , 20 years, Societal KA Benefits – Construction = Net Societal Savings
(Societal KA Benefits do not include other savings due to BCO Benefits)
7 YR Trend = 20.929x+297.3
x=Year 1 to 7
154 Sites equals 1.8% of all signalized intersection on the State Highway System
Reduction of 5 lives are applied to the based condition 297.3.
21 Lives Trend is from CARS Signalized intersection based on internal data 2011-2017
We did not have data before 2011 that we were able to use for this analysis.
Using 2019 Signalized Intersection TEO Data
Construction Cost is in NPV from a 20-year design Life.
Design, MOT, CEI, Mobilization, Contingency (Maintenance not included)
Future Analysis:
Initial Steps towards determining save cost implementation. Accuracy will increase with tracking of project after they are programmed and constructed, and calibrating benefit cost calculations will come from these values.

## Slide 4: Florida Roadway Safety Management
Federal safety funds categories (2017-2019)
  Highway Safety Improvement Program (HSIP)
  HSID
  HSLD
No formal process for candidate selections
  Based on project benefit-cost (B/C) ratios
Beginning 2024, Districts to fund safety projects following statutory requirements (pending)
SS2Z program to formalize and enhance roadway safety management
  Note: HSID stands for Highway Safety Improvement for Intersection Crashes
  HSLD stands for Highway Safety Improvement for Lane Departure Crashes

## Slide 5: What’s new in SAFE?
Florida specific Safety Performance Functions (SPF) for network screening
  Intersections grouped based on context classification, number of legs, and traffic control type
Data driven process for identifying safety projects
  Identify counterpart sister intersections
Diverging from hot-spot to predictive safety analysis
  Maximize benefits for FDOT safety funding
Countermeasures are identified and selected
  Projects are pre-approved for HSIP funding implementation
Definition
Candidate Intersections (poor safety performance)
Counterpart Sister Intersections (good safety performance)
Definition
Safety Performance Function (SPF) is an equation to calculate how many crashes are expected to occur, on average, for a selected roadway facility

## Slide 6: Methodology
6
Preliminary Diagnosis
Countermeasure Selection
Safety Effectiveness Evaluation
Project Prioritization
Economic Appraisal
Identify candidate intersections and their counterpart sister intersections
Develop SPFs using intersection traffic volumes, geometry,
and crash data
Calculate safety performance with
crash predictive models
FDOT Highway Safety Management Process
Network Screening
Annual Report
Implementation
Notes: Florida HSMP methodology uses AASHTO HSM fundamentals.

## Slide 7: On-system C4 4-leg Signalized Intersections
Major AADT: 59,000
Minor AADT: 25,733
4 KA crashes
Note: C4 = Urban general
AADT = Annual average daily traffic
Major AADT: 55,332
Minor AADT: 25,733
1 KA crash
7

## Slide 8: SAFE Report Contents
Priority locations
Proposed countermeasures
Days/months between expected fatal and severe injury crashes
Benefit-cost ratio (BCR)
Additional comments
Sister intersections
8
SAFE report available on the FDOT website
  https://bit.ly/2vmAezO

## Slide 9
SAFE Districts Overview
SHS Signalized Intersection Fatal and Severe Injuries
9
District | Total Candidates | Fatal & Severe (KA) |  | Fatal (K) | Severe (A) | Construction Cost (in millions)* | Annual Societal Benefits (in millions)
 |  | Expected | Reduction | Reduction | Reduction |  | 
1 | 22 | 50 | 10 | 19% | 19% | 5.2 | 14.6
2 | 8 | 12 | 3 | 22% | 23% | 2.6 | 4.5
3 | 2 | 3 | 1 | 36% | 36% | 0.9 | 1.8
4 | 26 | 45 | 9 | 19% | 19% | 5.9 | 16.2
5 | 47 | 93 | 13 | 13% | 13% | 13.0 | 19.3
6 | 18 | 29 | 6 | 19% | 19% | 1.1 | 10.5
7 | 31 | 64 | 8 | 12% | 12% | 11.7 | 11.6
Total | 154 | 296 | 50 | 16% | 16% | 40.4 | 78.5
* Construction cost is NPV for a 20-year design life

## Slide 10: SS2Z SAFE Report Snapshot
Candidate intersections and counterpart sisters

## Slide 11
Growing Partnerships
11

## Slide 12: SS2Z Next Steps
Develop SPFs for roadway segments, midblock crosswalks and bicycle facilities
Expand the analysis to include these facilities
Update SAFE Report annually (Dynamic Reporting)
Include more safety countermeasures when data is/are? available
Develop new sub-programs for STRIDES 2 Zero to enhance the overall safety management process
Notes: Pending CO funding availability.

## Slide 13: SS2Z 2020 Ask
  Districts, please use the SAFE 2020 Report to program and implement safety improvements at the listed intersections and provide feedback as to its usability
  Districts, please provide data for the missing intersections (i.e., local road AADTs, turn lanes, protective/permissive signal phasing, LPI, passive detection, etc.)
Notes: Bottom Line Ask:
1: Start using the tool to implement projects. Districts to send CO feedback to improve the tool.
2: Refine the tool by getting more data from the Districts to improve and enhance reliability. Including additional countermeasures.

## Slide 14
Javier Ponce
850-410-5417
Questions?
Trey Tillander
850-410-5419
Alan El-Urfali
850-410-5416
14